## Slide 1: Wing Design Regarding Mass and Drag
Dieter Scholz Hamburg University of Applied Sciences
Based on the Master Thesis of Houssein Mahfouz
SAWE 83rd International Conference on Mass Properties Engineering
Online, 20-22 May 2024
Paper 3801
https://doi.org/10.48441/4427.1587

## Slide 2: Abstract
    Purpose – To optimize the parameters of the wing of a jet transport aircraft with equations from the aircraft design on wing mass and drag in a spreadsheet (Excel) and with its optimizer (Solver).
    Methodology – The wing mass is calculated using Torenbeek's equation (with and without wing strut) and alternatively using an equation from the Luftfahrttechnischen Handbuch (LTH). Drag is divided into zero-lift drag, induced drag, and wave drag. The respective methods for calculating these drag elements are taken from Scholz's lecture notes. The aircraft design is mapped in a simplified way without the many hierarchically structured iterations. Instead, this simple wing design uses only one iteration. Procedures with snowball effect (Mass Growth Factor), with the 1st law of aircraft design and with both procedures combined are examined. On the one hand, the drag (fuel consumption) is minimized and, on the other hand, the take-off mass, which can be seen as a proxy for Direct Operating Costs (DOC).
    Findings – The simple approach to Multidisciplinary Design Optimization (MDO) is provided as a spreadsheet "Wing-MDO". In comparison with the complete aircraft design and optimization program "Optimization in Preliminary Aircraft Design" (OPerA), the results from the simpler "Wing-MDO" could be confirmed or calibrated to it. A further comparison resulted from the literature review. For an aircraft with parameters like the Airbus A320, an optimal wingspan is obtained by minimizing the drag of 42.52 m (-23.94 %) without a wing brace and 53.09 m (-24.50 %) using a wing brace and minimizing the take-off mass an optimal wingspan of 36.65 m (-8.76 %) or 44.20 m (-13.31 %). The resulting changes in drag or take-off mass are given in parentheses.

## Slide 3: Abstract
    Practical Implications – "Wing-MDO" is offered to the community as a simple and user-friendly tool in Excel for optimizing basic wing parameters.
    Social Implications – The optimization of an aircraft traditionally starts with the wing. This can currently also be seen in the new Boeing X-66A project. The present thesis serves to classify such proposals and shows that wings with a high span (and aspect ratio) can significantly reduce fuel consumption and thus CO2 emissions and environmental impact. Presented simple calculations make public discourse possible.
    Originality – Disciplines have presented the impact of their investigations at aircraft level, without considering the iterations (snowball effects) of aircraft design. Using the example of the wing, it could be shown how individual effects on mass and drag can be transferred simply but correctly to the aircraft level.

## Slide 4: Acknowledgment
    Houssein Mahfouz prepared a Master Thesis:
    "Einfacher Flügelentwurf optimiert hinsichtlich Masse und Widerstand"
    (Simple Wing Design Optimized for Mass and Drag)
    at
    Hamburg University of Applied Sciences,
    Aircraft Design and Systems Group (AERO).
    http://library.ProfScholz.de
    https://nbn-resolving.org/urn:nbn:de:gbv:18302-aero2023-10-16.018
Wing Design Regarding Mass and Drag

## Slide 5
Motivation
Wing Design Regarding Mass and Drag
Wing optimization is the classic first choice for optimization in classic aircraft design.
Wing optimization has two closely related disciplines: aerodynamics and structures.
The economics are always of most importance in commercial aviation
=> integration of economics as a third discipline.
In order to integrate these disciplines, the method of Multidisciplinary Design Optimization (MDO) is used. Traditionally, numerical methods such as Computational Fluid Dynamics (CFD) and Finite Element Method (FEM) have been used for this purpose.
This thesis investigates a simpler approach:
=> handbook equations are used for wing drag and wing mass
=> objective function is the take-off mass, which can be used as a proxy for the Direct Operating Costs (DOC).
How to integrate take-off mass into the optimization without the whole Aircraft Design loop, but instead using – much simpler – the mass growth factor?

## Slide 6
Table of Contents
Introduction Wing Design Optimized with Wing-MDO Wing Design Optimized in Aircraft Design with OPerA Comparison of the Results of Wing-MDO and OPerA Comparison of the Results of Wing-MDO and the Literature Review Efficient Wing with Large Wingspan for the Next Generation of Aircraft Conclusions and Outlook Contact List of References
Wing Design Regarding Mass and Drag

## Slide 7
    Introduction
Wing Design Regarding Mass and Drag

## Slide 8
Objectives and Research Questions
Introduction
Development of a sound understanding of simple Multidisciplinary Design Optimization (MDO) in aircraft design. Consideration of equations from aircraft design (zero lift drag, wave drag, induced drag and wing mass) to model wing MDO in Excel.
Research questions:
    Is it possible to obtain practical, optimized wing parameters if, instead of the numerical methods (CFD and FEM), only equations from the aircraft design are used and aircraft design iterations are only taken into account by a Mass Growth Factor?
    Optimization only with Excel's Solver and determination of relevant objective function for results (maximum take-off mass).
Comparison of the Wing-MDO tool to be created with the existing aircraft design optimizer OPerA (from PhD program).
Performing a literature review to support the comparison!

## Slide 9
    Wing Design
    Optimized with Wing-MDO
Wing Design Regarding Mass and Drag

## Slide 10
Description of Wing-MDO
Wing Design Optimized with Wing-MDO
Multidisciplinary Design Optimization (MDO) Program
User-friendly Excel file
Calculation of wing mass, drag coefficients (zero-lift drag, wave drag, induced drag), and drag
Two separate mass estimation methods:
=>Torenbeek Method => LTH Method
Set up with 20 Iteration Steps for Wing Mass Determination
Using the Excel Solver as a powerful optimization tool

## Slide 11
Parameter variation:
  Investigation of classic compromises in wing design,
  Variation of parameters: wingspan, relative thickness, taper, sweep, wing loading, Mach number and flight altitude,
  The user sets the range in which parameters are changed.
Two program versions:
  Wing-MDO-1: Focus on minimization of drag,
  Wing-MDO-2: Overcoming the challenges of minimizing take-off mass.
Description of Wing-MDO
Wing Design Optimized with Wing-MDO

## Slide 12
Wing-MDO-1 Layout (Screenshot):
Similarity in user interface and table structure of Wing-MDO-1 and Wing-MDO-2
Description of Wing-MDO
Wing Design Optimized with Wing-MDO

## Slide 13
Use of the Snowball Factor to calculate the change in wing mass between iteration steps:
Calculation of the new take-off mass from one iteration steps to the other:
Wing-MDO-1
(1)
(2)
Wing Design Optimized with Wing-MDO

## Slide 14
Main goal: Solving the problem of take-off mass minimization experienced in Wing-MDO-1
  Identified problems with Wing-MDO-1:
    Wingspan tends towards zero
    Significant increase in relative thickness
  Cause: Failure to take fuel mass into account in the take-off mass calculation equation of Wing-MDO-1
Calculation of the take-off mass in Wing-MDO-2 using the "1st law of the aircraft design":
Calculation of the new operating empty mass:
Results show that both in (4) together with (3) overestimate the change in wing mass.
    => Introduction of a reduction factor in (4):
Wing-MDO-2
(5)
(4)
(3)
Wing Design Optimized with Wing-MDO

## Slide 15
Identification of , so that Wing-MDO-2 and OPerA achieve the same wingspan for a cantilever wing while minimizing take-off mass
=>
Introduction of a damping factor in (3) to cope with diverging iteration:
=> = 0.69 is a good value.
Wing-MDO-2
(6)
Wing Design Optimized with Wing-MDO
Notes: Während der Bearbeitung traten gelegentlich aufschwingende Iterationen auf. Dieses Problem wurde gelöst, indem ein Dämpfungsfaktor in Gleichung (3) eingeführt wurde, was zur Entstehung von Gleichung (6) führte.
Der Parameter 𝑘_(𝑘,𝑀𝐺) wurde so identifiziert, dass Wing-MDO-2 und OPerA die gleiche Spannweite für einen freitragenden Flügel bei der Minimierung der Abflugmasse erzielen.
Dies führte zu 𝑘_(𝑘,𝑀𝐺)=0,855.

## Slide 16
Concrete example:
  Optimization for cantilever and braced wing based on the standard configuration of the A320-200
Application of the LTH method:
  Aspect ratio out of range in this example
    => no meaningful results
    => LTH method not anymore taken into account
Torenbeek method chosen to continue optimization
Optimization Results
Wing Design Optimized with Wing-MDO

## Slide 17
Optimization Results (Wing-MDO-1)
Results of drag minimization of a cantilever wing
 | bgiven [m] | t/c [-] | λ [-] | ϕ25 [°] | M [-] | H [m] | A [-] | mMTO [kg] | SW [m2] | mW [kg] | Dmin [N] | % difference in drag after optimization
f (b) | 50,20 | - | - | - | - | - | 15,57 | 97214 | 161,89 | 11903 | 28702 | -11,54
f (t/c) | - | 0,190 | - | - | - | - | 9,51 | 73400 | 122,23 | 5876 | 31236 | -3,73
f (λ) | - | - | 0 | - | - | - | 9,30 | 75110 | 125,08 | 6323 | 31317 | -3,48
f (ϕ25) | - | - | - | 12,50 | - | - | 9,26 | 75385 | 125,54 | 6395 | 31731 | -2,20
f (M) | - | - | - | - | 0,73 | - | 9,07 | 77008 | 128,24 | 6818 | 31392 | -3,25
f (H) | - | - | - | - | - | 6858 | 9,07 | 77008 | 128,24 | 6818 | 25224 | -22,26
f (b, t/c) | 51,11 | 0,186 | - | - | - | - | 17,13 | 91545 | 152,45 | 10516 | 27320 | -15,80
f (b, λ) | 50,70 | - | 0 | - | - | - | 16,34 | 94457 | 157,30 | 11233 | 27399 | -15,55
f (b, ϕ25) | 51,17 | - | - | 9,92 | - | - | 16,64 | 94522 | 157,41 | 11249 | 27603 | -14,93
f (b, M) | 50,85 | - | - | - | 0,71 | - | 15,82 | 98170 | 163,48 | 12134 | 27316 | -15,81
f (b, H) | 38,98 | - | - | - | - | 7571 | 11,06 | 82537 | 137,45 | 8245 | 25022 | -22,88
f (t/c, ϕ25) | - | 0,186 | - | 12,09 | - | - | 9,68 | 72134 | 120,12 | 5544 | 30720 | -5,32
f (b, t/c, ϕ25) | 52,38 | 0,180 | - | 10,66 | - | - | 18,29 | 90090 | 150,03 | 10155 | 26515 | -18,28
f (b, ϕ25, M) | 52,91 | - | - | 9,26 | 0,71 | - | 17,38 | 96738 | 161,09 | 11788 | 26005 | -19,85
f (t/c, ϕ25, M) | - | 0,189 | - | 11,33 | 0,72 | - | 9,70 | 71980 | 119,87 | 5503 | 29502 | -9,07
f (t/c, ϕ25, H) | - | 0,138 | - | 21,54 | - | 7076 | 9,28 | 75240 | 125,30 | 6357 | 25130 | -22,55
f (b, t/c, ϕ25, M) | 54,74 | 0,185 | - | 9,84 | 0,70 | - | 19,50 | 92255 | 153,63 | 10691 | 24789 | -23,60
f (b, t/c, ϕ25, H) | 42,52 | 0,149 | - | 14,45 | - | 8570 | 13,22 | 82157 | 136,82 | 8148 | 24677 | -23,94
Wing Design Optimized with Wing-MDO

## Slide 18
Optimization Results (Wing-MDO-2)
Results for minimizing the take-off mass of a cantilever wing
 | bgiven [m] | ϕ25 [°] | M [-] | A [-] | SW [m2] | mW [kg] | mMTO,min [kg] | % difference in take-off mass after optimization
f (b) | 35,20 | - | - | 10,90 | 113,63 | 7130 | 68236 | -7,16
f (ϕ25) | - | 27,50 | - | 10,16 | 114,38 | 6957 | 68687 | -6,55
f (M) | - | - | 0,74 | 10,21 | 113,82 | 6817 | 68353 | -7,00
f (b, ϕ25, M) | 36,65 | 6,95 | 0,73 | 12,03 | 111,68 | 6986 | 67065 | -8,76
Wing Design Optimized with Wing-MDO

## Slide 19
    Wing Design
    Optimized in
    Aircraft Design
    with OPerA
Wing Design Regarding Mass and Drag

## Slide 20
Description of OPerA
Wing Design Optimized in Aircraft Design with OPerA
Development of OPerA (Optimization in Preliminary Aircraft Design) as part of Mihaela Nita's PhD Thesis, supervision: Prof. Scholz (Nita 2013). Main objective: Set up optimization for preliminary and conceptual aircraft design. OPerA includes various modules such as Parameter Estimation, Preliminary Sizing, Area Estimation, Interference Factors, Resistance Estimation, Mass Calculation, Fuel Consumption Calculation, Direct Operating Cost Calculation and more. Two types of optimization with genetic algorithm (differential evolution):
a) Built-in VBA algorithms or
b) Interface with Optimus. User can set control parameters, free parameters, and objective functions (e.g., cost minimization or fuel mass reduction) to determine optimal aircraft parameters according to mission requirements.

## Slide 21
Optimization of a Cantilever Wing Based on the A320-200
Results to minimize fuel mass
Results to minimize take-off mass
Results to minimize DOC
 | A [-] | ϕ25 [°] | M [-] | b [m] | mMTO [kg] | SW [m2] | mW [kg] | mF, min [kg] | % difference in fuel mass after optimization
f(A) | 18,56 | - | - | 50,24 | 81669 | 136,01 | 11417 | 13466 | -16,18
f(ϕ25) | - | 21,23 | - | 34,48 | 77296 | 125,15 | 6659 | 16045 | -0,13
f(M) | - | - | 0,72 | 34,68 | 76025 | 126,60 | 6238 | 15774 | -1,82
f (A, ϕ25, M) | 19,88 | 20,09 | 0,68 | 49,62 | 77056 | 123,83 | 9920 | 12674 | -21,12
 | A [-] | ϕ25 [°] | M [-] | b [m] | SW [m2] | mW [kg] | mMTO, min [kg] | % difference in take-off mass after optimization
f (A, ϕ25, M) | 12,01 | 7,04 | 0,65 | 36,65 | 111,92 | 6077 | 73594 | -5,29
 | A [-] | ϕ25 [°] | M [-] | b [m] | mMTO [kg] | SW [m2] | mW [kg] | CDOC,min [€/NM/t] | % difference in DOC after optimization
f (A, ϕ25, M) | 13,22 | 13,22 | 0,69 | 39,35 | 75507 | 117,06 | 7650 | 1,16 | -1,98
Wing Design Optimized in Aircraft Design with OPerA

## Slide 22
    Comparison of
    the Results of Wing-MDO and OPerA
Wing Design Regarding Mass and Drag

## Slide 23
Wing-MDO vs. OPerA
    Comparison of the Results of Wing-MDO and OPerA
Results to minimize drag, fuel mass, take-off mass, and DOC of a cantilever wing based on the A320-200
Comparable results of Wing-MDO and OPerA
Selection of tool depending on the specific objective function:
  Drag minimization: Wing-MDO-1 due to faster calculation.
  Minimization of take-off mass (proxy for DOC): Wing-MDO-2 is suitable (not Wing-MDO-1).
  Complete aircraft design with many parameters and DOC calculation: Use OPerA.
 | Objective functions with % difference after optimization |  | b [m] | ϕ25 [°] | M [-] | A [-] | mMTO [kg] | SW [m2] | mW [kg]
f (b, ϕ25, M),Wing-MDO-1 | Dmin | (-19,85) | 52,91 | 9,26 | 0,71 | 17,38 | 96738 | 161,10 | 11788
f (A, ϕ25, M),OPerA | mF,min | (-21,12 ) | 49,62 | 20,09 | 0,68 | 19,88 | 77056 | 123,83 | 9920
f (b, ϕ25, M),Wing-MDO-2 | mMTO,min | (-8,76) | 36,65 | 6,95 | 0,73 | 12,03 | 67065 | 111,68 | 6986
f (A, ϕ25, M),OPerA | mMTO,min | (-5,29 ) | 36,65 | 7,04 | 0,65 | 12,01 | 73594 | 111,92 | 6077
f (A, ϕ25, M),OPerA | CDOC,min | (-1,98) | 39,35 | 13,22 | 0,69 | 13,22 | 75507 | 117,06 | 7650
Notes: Die Ergebnisse zur Minimierung von Widerstand, Kraftstoffmasse, Abflugmasse und DOC eines freitragenden Flügels basierend auf der Standardkonfiguration der A320-200 unter Verwendung von Wing-MDO und OPerA sind auf dieser Folie zusammengefasst.
Es zeigt sich, dass die Minimierung des Widerstands mithilfe von Wing-MDO-1 eine Spannweite von etwa 52,9 m erzielte, während OPerA eine Spannweite von etwa 49,6 m erzielte, um die Zielfunktion der Kraftstoffmassenminimierung zu erfüllen. Die Differenz zwischen diesen Werten beträgt 3,3 m, was einer prozentualen Abweichung von nur 6,65 % entspricht.
Die Minimierung der Abflugmasse mithilfe von Wing-MDO-2 führte zu einer Spannweite von 36,65 m. Es ist anzumerken, dass der Parameter 𝑘_(𝑘,𝑀𝐺) so angepasst wurde, dass sowohl Wing-MDO-2 als auch OPerA dieselbe Spannweite bei der Abflugmassenminimierung aufwiesen, wie zuvor erwähnt. Trotz dieser Angleichung gibt es Unterschiede in anderen Parametern zwischen Wing-MDO-2 und OPerA.
Zum Beispiel betrug die berechnete Machzahl bei Wing-MDO-2 0,73, während OPerA einen Wert von 0,65 aufwies. In Bezug auf die Abflugmasse belief sich der Wert bei Wing-MDO-2 auf 67065 kg, während OPerA 73594 kg ergab.
Die Minimierung der DOC unter Verwendung von OPerA führte zu einer Spannweite von 39,35 m. Der prozentuale Unterschied zwischen dieser Spannweite und derjenigen, die bei der Abflugmassenminimierung mit Wing-MDO-2 erzielt wurde, beträgt lediglich 7,23 %.
Diese Ergebnisse zeigen, dass sowohl Wing-MDO als auch OPerA vergleichbare Ergebnisse erzielen.
Die Auswahl zwischen den Programmen (Wing-MDO-1, Wing-MDO-2 und OPerA) hängt von der spezifischen Zielfunktion ab.
Wenn der Schwerpunkt auf der Widerstandsminimierung liegt, könnte Wing-MDO-1 aufgrund seiner schnelleren Berechnungen bevorzugt werden.
Andererseits, wenn die Zielfunktion auf die Minimierung der Abflugmasse abzielt, die als Ersatzgröße für die direkten Betriebskosten (DOC) dienen kann, könnte Wing­‑MDO­-2 genutzt werden.
Wenn jedoch ein vollständiger Flugzeugentwurf erforderlich ist, der viele Iterationen und eine umfassende DOC-Berechnung erfordert, dann müsste OPerA genutzt werden.

## Slide 24
    Comparison of
    the Results of Wing-MDO and a Literature Review
Wing Design Regarding Mass and Drag

## Slide 25
Master Thesis of Hoogervorst 2015 (TU Delft)
    Comparison of the Results of Wing-MDO and a Literature Review
Titel:
Wing Aerostructural Optimization Using the Individual Discipline Feasible Architecture.
Objective: Minimizing drag by optimizing the wing geometry of the Airbus A320.
Approach used: Applying the Individual Discipline Feasible (IDF) architecture to solve a gradient-based multidisciplinary design optimization problem.
Advantage of IDF architecture: Does not require coupled sensitivity analysis for gradient-based optimization, allowing for greater flexibility in choosing software for disciplinary analysis and reducing overall computational costs.
Software tools used:
  Aerodynamics: SU2 software for deformation of surface and volume lattices, calculation of flow properties and derivation of sensitivities.
  Structure: FEMWET software to model the static aeroelastic deformation and aeroelastic axis of the wing.

## Slide 26
Wing-MDO-1 Compared to Hoogervorst 2015
Results of drag minimization of a cantilever wing achieved by Wing-MDO-1 and Hoogervorst 2015
Comparable results despite different optimization approaches.
Optimization with Wing-MDO-1 is faster than the optimization carried out in the study by Hoogervorst 2015.
 | b/2 [m] | ϕ25 [°] | A [-] | mMTO [kg] | SW [m2] | mW [kg] | CD [-]
Wing-MDO-1 | 21,26 | 14,4 | 13,22 | 82157 | 68,40 | 8148 | 0,0136
Hoogervorst 2015 | 19,57 | 20,2 | 11,55 | 70948 | 66,32 | 8270 | 0,0142
% Difference | 8,64 | 28,71 | 14,46 | 15,80 | 3,14 | 1,48 | 4,23
    Comparison of the Results of Wing-MDO and a Literature Review

## Slide 27
    Efficient
    Large Span Wing
    for the
    Next Generation
    of Aircraft
Wing Design Regarding Mass and Drag

## Slide 28
Efficient Wing
    Efficient Large Span Wing for the Next Generation of Aircraft
Drag: Optimization vs. Standard A320-200 for Cantilevered and Braced Wing
A braced wing is more efficient than a cantilever wing.
Recommended span: 36 m to 52 m (ICAO code D).
Chart: D [N] Vergleichswiderstand
| Standardkonfiguration der A320-200 | f(b) | f(t/c) | f(ϕ25) | f(M) | f(H) | f(b, t/c, ϕ25, H)
Freitragender Flügelwiderstand | 32445.7416 | 28701.8822 | 31236.3818 | 31730.9097 | 31391.9702 | 25224.2778 | 24677
Abgestützter Flügelwiderstand | 26346.5544 | 21067.296 | 25995.8042 | 26079.433 | 25409.7877 | 21305.4771 | 19890.407

## Slide 29
Boeing's Innovative Aircraft Project (Boeing X-66A)
Boeing is working on a successor for the B737 Max in cooperation with NASA. This project, called the "Sustainable Flight Demonstrator", uses the innovative "Transonic Truss-Braced Wing" concept, known as the X-66A. (Bardan 2023, Ebner 2023, Sebayang 2023). Boeing X-66A is to be equipped with a folding braced wing with a high aspect ratio and
wingspan of approximately 52 m. (Boeing 2019) Goal: Reduction of drag and integration of more efficient components (e.g. propulsion systems)
Boeing X-66A (Boeing 2019)
    Efficient Large Span Wing for the Next Generation of Aircraft

## Slide 30
    Conclusions
    and
    Outlook
Wing Design Regarding Mass and Drag

## Slide 31
    Conclusions and Outlook
The master thesis helps to understand wing optimization in aircraft design and shows that practical and optimum wing parameters can be found by using only handbook equations from aircraft design instead of numerical methods. The aircraft design iteration is taken into account by a snowball factor (mass growth factor) and optimization with the Solver in Excel.
Ideas for future research:
  Identifying different values for the reduction factor to achieve specific objectives:
      To achieve comparable results in drag minimization between Wing-MDO-1 and Wing-MDO-2 (instead of Wing-MDO-2 and OPerA).
      Ensuring comparable results between Wing-MDO-2 and OPerA for different aircraft types and a wide range of parameters, not only for taking into account wingspan.
  Investigation of efficient engines integrated into braced wings using OPerA and its practical aircraft design approach.
Wing Design Regarding Mass and Drag
Notes: Diese Masterarbeit hilft beim Verständnis der Flügeloptimierung im Flugzeugentwurf und zeigt auf, dass praxisgerechte und optimale Flügelparameter erreicht werden können, indem ausschließlich Gleichungen aus dem Flugzeugentwurf anstelle von numerischen Methoden verwendet werden. Dabei wird der Flugzeugentwurf durch einen Schneeballfaktor (Mass Growth Factor) berücksichtigt.
Zukünftige Forschungsbemühungen sollten darauf abzielen, den Parameter 𝑘_(𝑘,𝑀𝐺) so zu identifizieren, dass sowohl Wing-MDO-1 als auch Wing-MDO-2 vergleichbare Ergebnisse bei der Minimierung des Widerstands erzielen können. Parallel dazu ist die Identifikation anderer Werte für 𝑘_(𝑘,𝑀𝐺) erforderlich, um sicherzustellen, dass Wing-MDO-2 und OPerA vergleichbare Ergebnisse für verschiedene Flugzeugmodelle und eine Vielzahl von Parametern erzielen können, wobei nicht nur die Spannweite berücksichtigt wird. Darüber hinaus sollte eine detaillierte Analyse der Variation von 𝑘_(𝑘,𝑀𝐺) durchgeführt werden. Weiterhin könnte die Optimierung weiter verfeinert werden und die Integration von abgestützten Flügeln und effizienten Triebwerken in realen Flugzeugdesigns untersucht werden.

## Slide 32
info@ProfScholz.de
http://mass.ProfScholz.de and http://library.ProfScholz.de
Contact
Quote this document:
SCHOLZ, Dieter, 2024. Wing Design Regarding Mass and Drag. In: Society of Allied Weight Engineers (SAWE), 83rd
International Conference on Mass Properties Engineering. Online, 20-22 May 2024.
Available from: https://doi.org/10.48441/4427.1587
Quote the thesis:
MAHFOUZ, Houssein, 2023. Einfacher Flügelentwurf optimiert hinsichtlich Masse und Widerstand.
Masterarbeit. Aircraft Design and Systems Group (AERO), HAW Hamburg, 2023-10-30.
Available from: https://nbn-resolving.org/urn:nbn:de:gbv:18302-aero2023-10-16.018
 Copyright by Author, CC BY-NC-SA, https://creativecommons.org/licenses/by-nc-sa/4.0
Wing Design Regarding Mass and Drag

## Slide 33
    List of References
BARDAN, Roxana, 2023. NASA Issues Award for Greener, More Fuel-Efficient Airliner of Future. NASA | 
Available from: | https://go.nasa.gov/3QiFStn
Archived at: | https://perma.cc/YMC7-QTNP
BOEING, 2019. Spreading our wings: Boeing unveils new Transonic Truss-Braced Wing. | 
Available from: | https://bit.ly/3qXKqeP
Archived at: | https://perma.cc/5KA2-7HG9
EBNER, Ulrike, 2023. Transonic Truss-Braced Wing heißt nun X-66A. In: Flugrevue, 2023-06-13. | 
Available from: | https://bit.ly/3RXVVxR
Archived at: | https://perma.cc/BP9N-A8Z2
NITA, Mihaela Florentina, 2013. Contributions to Aircraft Preliminary Design and Optimization. Dissertation. München: Verlag Dr. Hut. | 
Available from: | https://purl.org/aero/NITA_DISS_2013
SEBAYANG, Andreas, 2023. Boeing und Nasa wollen "Sustainable Flight Demonstrator" bis 2030 in die Luft bringen. Airliners.de. | 
Available from: | https://bit.ly/48Wf09H
Archived at: | https://perma.cc/2LJX-UL8G
Wing Design Regarding Mass and Drag